## Slide 1: The 11th Public and Private Joint Forum In Asian Region (January 26-27, 2021) Country Report on 'Recent situation of the measures related to vehicle safety and environment' India

## Slide 2
Government of India
MORTH
Ministry of Road Transport & Highways
MOHI
Ministry of Heavy Industries & Public Enterprises
MOEF
Ministry of Environment & Forests
Ministry of Consumer Affairs
DGFT
Director General Foreign Trade
State Ministries
Standardization
CMVR-
Technical Standing Committee
Automotive Industry Standards Committee-AISC
Standing Committee on Emission Legislation- SCOE
Bureau of Indian Standards-BIS
Certification Agencies
1. ARAI – The Automotive Research Association of India
2. VRDE – Vehicle Research Development Establishment
3. CIRT – Central Institute of Road Transport
4. ICAT – International Centre for Automotive Technology
5. IIP – Indian Institute of Petroleum
6. CFMTTI – Central Farm Machinery Testing & Training Institute
7. NRFMTTI – Northern Region Farm Machinery Testing &
Training Institute
8. GARC – Global Automotive Research Centre (GARC)
9. NATRAX – National Automotive Test Tracks
Regulatory Mechanism - Stakeholders

## Slide 3
National Committees
Various National committees monitor the work related to automotive regulations.
01
Apex Committees working on Safety and Emission Regulations
CMVR-TSC & SCOE
02
Subsidiary Committee to CMVR-TSC and SCOE for formulating and approving standards
AISC
03
Group of Experts supporting AISC and BIS for formulating Standards
Technical Panels
04
Harmonization of Standards
India WP.29 Activities
AIS
CMVR
IS
UN R
UN GTR
MVA
MVA Motor Vehicle Act
CMVR Central Motor Vehicle Rules
IS Indian Standards
AIS Automotive Industry Standards
UN GTR UN Global Technical Regulations
UN R UN Regulations
Regulatory Mechanism - Stakeholders

## Slide 4: National Committees - Composition
MoRT&H
Standing Committee on Emissions (SCoE)
Chairman: Joint Secretary (MoRT&H)
Members: MoP&NG, MoHI&PE, MoEF, NATRiP, Test Agencies, SIAM, TMA & Others
National Standing Committee
on WP.29
Chairman: Joint Secretary (MoRT&H)
Members: MoHI&PE, MoEF, DoC, DIPP, NATRiP, Test Agencies, BIS, SIAM, TMA, ACMA & Others
CMVR-Technical Standing Committee (CMVR-TSC)
Chairman: Joint Secretary (MoRT&H)
Members: MoHI&PE, NATRiP, Test Agencies, BIS, SIAM, TMA, ACMA & Others
Automotive Industry Standard Committee (AISC)
Chairman: Director (ARAI)
Members: MoRT&H, MoHI&PE, MoSSI, NATRiP, Test Agencies, BIS, SIAM, TMA, ACMA & Others

## Slide 5: Features of Indian Type Approval System
Type Approval system is similar to UN-ECE
  Implemented in year 1991
Type Approval administration
  Notifying agencies: Primarily MoRTH
  Standards and other requirements are notified under CMVR
  Testing agencies: Notified under Rule 126
  TA certificates: Issued by Testing Agencies
Test standards
  Bureau of Indian Standards (BIS) prepares IS standards
  AISC Technical committee prepares AIS standards as an interim step
  Emission Test Procedure as per TAP/ 115-116 Document. Future standards will be published as AIS.
Roadmap of Regulations
  Agreed by industry, test agencies and government
  Standards are aligned with UN Regulations / Global Technical Regulations (GTR) to the extent possible

## Slide 6
Social Requirements
International Harmonization
Inputs from National Committees
National
Rules / Act
Technological Advancement
Ministry of Road Transport & Highways is the nodal Ministry for motor vehicle regulations in India
Governing Factors

## Slide 7
Key provisions in Motor Vehicles (Amendment) Act, 2019
Mandatory fitness test through Automated Centres
New provision for ELV
New Section on Vehicle Recall
Safety of Pedestrians and Non Motorized Transport
Safety of Children during Commute
Electronic Monitoring and Enforcement of Road Safety
New Section for Good Samaritan, Golden Hour treatment, No fault liability
Penalties
Schemes for interim relief for accident victim claimants
Constitution of Motor Vehicle Accident relief Fund
Formulation of Road Safety Board
Various Central Motor Vehicle Rules concurrent with Motor Vehicle (Amendment) Act, 2019 are under process.
Motor Vehicle (Amendment) Act, 2019

## Slide 8
professional drivers' work conditions
Recommended actions to strengthen cooperation &
coordination towards global road safety
develop national, regional & global targets to reduce road traffic crashes & fatalities. (WHO, UNECE, Stakeholders)
Recommended actions to increase awareness &
build capacity of road users
Recommended actions to develop & promote the use of safer vehicles
seat belts, air bags and active safety systems such as ABS & ESC fitted as standard, air quality, vehicle disposal
India’s Safety Commitments
Excerpts from Brasilia Declaration
India is a signatory to Brasilia Declaration and is committed to reduce the number of road accidents and fatalities.
- Reference – Report : Road Accidents in India 2015 – MoRTH

## Slide 9
The child restraint regulation
5
The seat-belt regulation
4
Pedestrian front protection
3
Electronic Stability Control
2
Frontal impact protection and side impact protection
1
Objective:
Eliminate production (and importation) of substandard new vehicles.
Target:
100% of new vehicles (defined as produced or sold) meeting priority standards (based on UN regulations or equivalent recognised national standards).
Core Area - Safer Vehicles
Motorcycle antilock braking systems
6
Candidate global targets and indicators for review

## Slide 10
Accident Statistics (India)
2008
Road Accidents
4,84,704
Persons Injured
5,23,193
Fatalities 1,19,860
Every hour
55 accidents &
14 deaths
2018
Road Accidents
4,67,004
Persons Injured
4,69,418
Fatalities 1,51,417
Every hour
53 accidents &
17 deaths
Source: MoRTH - Road Accidents in India (2008 & 2018)
2018 Vs 2008
Fatalities
2018 Vs 2015
Road Accidents, Persons Injured

## Slide 11
Years | Population of India (in thousand) | Road Accident Risk (normalized for pop)* | Road Accident Death Risk (normalized for pop)$ | Total number of registered vehicles (in thousand) | Road accident Rate (normalized for vehicles)# | Road accident death rate (normalized for vehicles)## | Vehicle Density $$
1990 | 8,35,000 | 33.8 | 6.5 | 19,152 | 147.6 | 28.2 | 10
2000 | 10,14,825 | 38.6 | 7.8 | 48,857 | 80.1 | 16.2 | 15
2005 | 10.95,722 | 40.1 | 8.7 | 81,502 | 53.9 | 11.7 | 21
2010 | 11,76,742 | 42.5 | 11.4 | 1,27,746 | 39.1 | 10.5 | 28
2015 | 12,54,019 | 40.0 | 11.7 | 2,10,023 | 23.9 | 7.0 | 38
2016 | 12,68,961 | 37.9 | 11.9 | 2,30,031 | 20.9 | 6.6 | 41
2017 | 12,83,601 | 36.2 | 11.5 | 2,53,311 | 18.4 | 5.8 | 43
2018 | 12,98,043 | 36.0 | 11.7 | -- | -- | -- | --
*Road Accident Risk : Number of accidents per lakh population
$Road Accident Death Risk : Number of persons killed per lakh population
#Road Accident Rate : Number of accidents per ten thousand vehicles
##Road Accident Death Rate : Number of persons killed per ten thousand vehicles
$$Vehicle Density : Number of Vehicles per km of Road
≈3 times reduction
≈3 times increase
Fatality Vs Vehicle Population
Source: MoRTH - Road Accidents in India (2018)

## Slide 12: Safety Norms – History / Future
2010-15
2005-10
2000-05
2015-20
2020-
  Brakes / High speed Braking
  Steering Effort
  Seat Belt & Anchorages
  Gradeability
  Tell tales & Controls
  Lighting
  Pass by noise
  CoP of components
  Survival Space
  Strength of Superstructure
  Retro-reflectors
  Safety - BoV
  Spray suppression
  Demist & Defrost
  Traction Batteries
  EMC
  Crash Norms
  Airbags, CRS
  Speed and seat belt alert
  Pedestrian Safety
  ABS
  EMI / EMC
  AHO
  Sleeper Coaches
  Double Deck Buses
  ESC
  Safety Roadmap for CEVs
  Safety features for 2 W – Stands, Foot rest, external projections
  Future Subjects
    AEBS
    ADAS
    New Technologies
Significant Step in last 5 years

## Slide 13
1
2
3
4
5
6
Airbag
Driver Airbag is mandatory
Seat Belt Reminder
Driver and Co Driver Seat Belt Reminder
Manual Override for Central Locking
Manual override for protection against lock down
Crash Standards
Mandatory Crash Standards.
Rear Parking Assist System
RPAS for safe parking
Pedestrian safety
Car design for ensuring pedestrian safety in event of crash
Passenger Car – Key New Requirements

## Slide 14: Main slide – used for hyperlink interaction do not delete
ABS for almost all
categories of vehicles
Brake Assist Systems - If fitted for M1 and N1
Braking
Electronic Stability Control System
If fitted for M1/N1 &
Mandatory for Buses
Revised Braking Standards fro All Categories of Vehicles
ABS or CBS for two Wheelers
Safety Requirements - Braking

## Slide 15
Construction Safety
Scope: M & N category
In CMVR: AIS 038 (Rev. 1)
New Adopted : AIS 038 (Rev. 2)
Inline with GTR 20 Phase 1 and UN R 100 Rev 3 Transposition Document
Proposed for Notification
AIS 038 (Rev. 2)
Construction Safety
Scope: L category
In CMVR: AIS 038 (Rev. 1)
New Adopted: AIS 156
Inline with UN R 136
Proposed for Notification
AIS 156
Measurement of Electrical Energy Consumption
Scope: L, M & N category
In CMVR: AIS 039 (Rev. 1)
Inline with UN R 101 Rev. 3
AIS 039 (Rev. 1)
Measurement of Net Power & Maximum 30 Minute Power
Scope: L, M & N category
In CMVR: AIS 041 (Rev. 1)
Inline with UN R 85
UN R 85 Rev. 1 available
(No technical change
for Motor)
AIS 041 (Rev. 1)
Measurement of Range
Scope: L, M & N category
In CMVR: AIS 040 (Rev. 1)
Inline with UN R 101 Rev. 3
AIS 040 (Rev. 1)
Electric Vehicles

## Slide 16
A
B
C
D
E
F
G
Interior Noise, Vibration and Harshness
Braking Performance & Vehicle Stability Function
Fire Detection & Alarm System Fire Detection & Suppression System
Requirements for kneeling system, Ramp, Lift for person with reduced mobility
Requirements for Priority Seats & Space for Passengers with Reduced Mobility
Requirements for wheelchair and its accommodation for person with reduced mobility
Emergency Lighting System
Advance Requirements for Buses (To Improve Public Transport)

## Slide 17
Codes for Truck and Trailers
Requirements for Truck Cabin and Load Body
Requirements for Trailers
Focus on improving the Logistics Segment to enhance safety as well as efficiency.

## Slide 18
Specific Codes for Special Purpose Vehicles
Ambulance Code
School Bus
Sleeper Coaches
Motor Caravan
Double Deck Buses
Reefer Van
Food Truck
Cash Vans
Special Purpose Vehicles

## Slide 19
Safety Features in Motorcycles
AIS 146 (Stands) : Reference Standard Annex XVI of EU directive 44/2014. Stability Requirement, Durability, Automatic Retraction while vehicle moving or disable vehicle propulsion if side stand is on.
AIS 147 (External Projections) : Reference Standard : Annex VIII of EU directive 44/2014.
AIS 148 (Foot Rest) : Reference Standard : Annex XIII of EU directive 44/2014. Strength Requirement.
Implementation from January 2022.
Stands
External Projections
Foot Rest
AIS146
AIS 147
AIS 148

## Slide 20
Key Emission norms notified in India
Implementation of Bharat Stage VI (BS VI) emission norms for L, M and N category vehicles.
Real Driving Emissions.
Next Stage Emission Norms for Agricultural Tractors, CEV and Combine Harvester.
Alternate Fuels such as Methanol, Ethanol, Dual Fuel, LNG, Bio-diesel, CNG and Bio-CNG.
Emission Regulations

## Slide 21
10 ppm entire country BSVI Nationwide-2020
2500 ppm sulphur in NCR- 1997
5000 ppm sulphur 4 metro cities- 1996
50 ppm 11 cities & 350 ppm Nationwide, (BSIV)-2010
350 ppm 11 cities & 500 ppm entire country (BSIII)-2005
500 ppm sulphur 11 cities -2004
2500 ppm sulphur entire country(BSI) -2000
2500 ppm in 4 metro cities -1998
50 ppm entire country BSIV Nationwide-2017
Market Fuel Diesel Sulphur Content
250 times reduction
Advancement
through 20 years

## Slide 22
Key Safety provisions notified in India
Emissions
Diesel with Compressed Natural Gas (CNG) or Bio-Compressed Natural Gas (Bio-CNG) or Liquefied Natural Gas (LNG) as dual fuel
  - Mass emission standards for Di-Methyl Ether (DME or D100) Vehicles
  - Mass emission provisions for M85 Vehicles
Implementation of BS VI norms for Quadricycles. From 22nd May 2020.
OBD monitoring items for BS VI from 1st April 2020.
OBD Stage II-A Thresholds for BS-VI vehicles from 1st April 2023.
OBD Stage II-B Thresholds for BS-VI vehicles from 1st April 2025
CNG/Bio CNG/HCNG as per AIS 024 & 028 (Rev.1) and fuel specs as per IS 17314:2019 from 25th September 2020
Safety
Approval of HSRP as per AIS-159 from 11th February 2020
Overall Dimensions of Motor Vehicle 26th June 2020.
Safety Glazing for materials conforming to IS 2553 (Part 2) from 1st April 2021.
Tyre Pressure Monitoring System as per AIS 154, from 1st October 2020.
Puncture repair kit for M1 category with tubeless Tyres from 20th July 2020.
Hydrogen Fuel Cell Vehicles for Category M and N as per AIS 157: 2020 from 23rd September 2020.
Safety Regulations for Construction Equipment Vehicles
Snapshot of various regulations to be implemented

## Slide 23
Setting up of model in - use vehicle Inspection and Certification Test Centers at various places in the country is in progress.
AIS-129 on End of Life of Vehicles is published and implementation plan is under discussion.
Draft Guidelines for setting up Authorized Vehicle Scrapping Facility has been issued.
Control of In-Use Vehicles

## Slide 24
Thank You !